Network Emulator in Linux
Using Linux NetEm to emulate a network

---
Network Parameters
Delay/Jitter

---
Network Parameters
Packet Loss

---
Network Parameters
Corruption

---
Network Parameters
Duplication

---
Network Parameters
Reorder

---
Network Parameters
Bandwidth

---
Network Parameters
Base for all commands
tc qdisc add dev <dev> root netem <command>
tc qdisc replace dev <dev> root netem <command>
Deleting all NetEm directives
tc qdisc del dev <dev> root netem
Showing current queue discipline
tc qdisc show dev <dev>

---
Delay/Jitter

---
Delay/Jitter
- A delay is a latency added to the packet
- A jitter is a variance in the delay over time
- The delay is added by the processing time of routing devices in between
- The jitter is added by different load of the routing devices

---
Delay/Jitter
Simulating a delay (in ms) with NetEm
<base> delay <delay>
Simulating a jitter (in ms) (together with a delay) with NetEm
<base> delay <delay> <jitter>
Samples
... netem delay 10ms
... netem delay 10ms 5ms

---
Packet Loss

---
Packet Loss
- netem supports three loss models
  - Independent loss
  - Markov model
  - Gilbert-Elliott model

---
Packet Loss
- The independent loss
- For every single packet an probability of loss is applied
- Simulating an independent loss with netem
<base> loss random <percentage>
Samples
... netem loss random 2%

---
Packet Loss
- The Markov model and the Gilbert-Elliott model work with states
- The models differentiate between a Gap (or Good) state and a Burst (or Bad) state
- In Burst state all or most packets are lost
- In Gap state all or most packets are transmitted

---
Packet Loss
The Markov model
- 1 (or G) means Gap or Good (Packet is transmitted)
- 3 (or B) means Burst or Bad (packet is lost)
- 2 means packet is transmitted during burst
- 4 means packet is lost during gap
4
1
G
3
B
2
p13
p31
p32
p23
p14

---
Packet Loss
The Markov model
- p13 is the probability from G to B
- p31 is the probability from B to G
- etc
4
1
G
3
B
2
p13
p31
p32
p23
p14

---
Packet Loss
- The Gilbert and Gilbert-Elliott model
- G means Gap or Good
- B means Burst or Bad
- p is the probability from G to B
- r is the probability from B to G
- 1-k is the probability of a loss in G
- 1-h is the probability of a transmit in B
G
1-k
B
1-h
p
r

---
Packet Loss
Simulating a loss with a Markov model
<base> loss state <p13> [<p31> [<p32> [<p23> [<p14>]]]]
Samples
... netem loss state 1%
... netem loss state 1% 5%
... netem loss state 1% 5% 10% 50% 2%
4
1
G
3
B
2
p13
p31
p32
p23
p14

---
Packet Loss
Simulating a loss with Gilbert-Elliott model
<base> loss gemodel <p> [<r> [<1-h> [<1-k>]]]
Samples
... netem loss gemodel 1%
... netem loss gemodel 1% 5%
... netem loss gemodel 1% 5% 10% 10%
G
1-k
B
1-h
p
r

---
Corruption

---
Corruption
- During processing a packet can get corrupted
- Simulating a certain percentage of corruption
<base> corrupt <percentage>
Samples
... netem corrupt 1%

---
Duplication

---
Duplication
- During processing a packet can get duplicated (e.g. resent)
- Simulating a certain percentage of duplication
<base> duplicate <percentage>
Samples
... netem duplicate 1%

---
Reorder

---
Reorder
- During processing two packets can be reordered
- Reorder only works if also a delay is specified
- Simulating a certain percentage of reorder
<base> reorder <percentage>
Samples
... netem delay <delay> reorder 25%
This example sends 25% of the packages directly and 75% are delayed

---
Bandwidth

---
Bandwidth
- A (symmetric) bandwidth limitation can also be emulated
- Additionally a repackaging of data can be emulated (e.g. other MTU)
- Simulating a bandwidth limitation
<base> rate <bandwidth> [<overhead> [<cellsize> [<celloverhead>]]]
Samples
... netem rate 1Mbit
... netem rate 1Mbit 5
... netem rate 1Mbit 5 128

---
References
- http://voiptroubleshooter.com/indepth/burstloss.html
- http://voiptroubleshooter.com/indepth/jittersources.html
- https://www.net.t-labs.tu-berlin.de/papers/HH-GEMPLRTSI-08.pdf